## Slide 39
Features | Memory Mapped IO | IO Mapped IO
Addressing | IO devices are accessed like any other memory location. | They cannot be accessed like any other memory location.
Address Size | They are assigned with 16-bit address values. | They are assigned with 8-bit address values.
Instructions Used | The instruction used are LDA and STA, etc. | The instruction used are IN and OUT.
Cycles | Cycles involved during operation are Memory Read, Memory Write. | Cycles involved during operation are IO read and IO writes in the case of IO Mapped IO.
Registers Communicating | Any register can communicate with the IO device in case of Memory Mapped IO. | Only Accumulator can communicate with IO devices in case of IO Mapped IO.

## Slide 40
Features | Memory Mapped IO | IO Mapped IO
Space Involved | 216 IO ports are possible to be used for interfacing in case of Memory Mapped IO. | Only 256 I/O ports are available for interfacing in case of IO Mapped IO.
IO/M` signal | During writing or read cycles (IO/M` = 0 ) in case of Memory Mapped IO. | During writing or read cycles (IO/M` = 1) in case of IO Mapped IO.
Control Signal | No separate control signal required since we have unified memory space in the case of Memory Mapped IO. | Special control signals are used in the case of IO Mapped IO.
Arithmetic and Logical operations | Arithmetic and logical operations are performed directly on the data in the case of Memory Mapped IO. | Arithmetic and logical operations cannot be performed directly on the data in the case of IO Mapped IO.

## Slide 41
Basis for Comparison | Memory mapped I/O | I/O mapped I/O
Basic | I/O devices are treated as memory. | I/O devices are treated as I/O devices.
Allotted address size | 16-bit (A0 – A15) | 8-bit (A0 – A7)
Data transfer instructions | Same for memory and I/O devices. | Different for memory and I/O devices.
Cycles involved | Memory read and memory write | I/O read and I/O write
Interfacing of I/O ports | Large (around 64K) | Comparatively small (around 256)
Control signal | No separate control signal is needed for I/O devices. | Special control signals are used for I/O devices.
Efficiency | Less | Comparatively more
Decoder hardware | More decoder hardware required. | Less decoder hardware required.

## Slide 42
Basis for Comparison | Memory mapped I/O | I/O mapped I/O
IO/M’ | During memory read or memory write operations, IO/M’ is kept low. | During I/O read and I/O write operation, IO/M’ is kept high.
Data movement | Between registers and ports. | Between accumulator and ports.
Logical approach | Simple | Complex
Usability | In small systems where memory requirement is less. | In systems that need large memory space.
Speed of operation | Slow | Comparatively fast
Example of instruction | LDA ****H STA ****H MOV A, M | IN ****H OUT ****H